## Slide 1
MERIDIAN SOLAR IPP | 50 MW | INTERNAL DEAL REVIEW
Do not proceed to credit committee on current terms
The financing works; the asset economics do not — project IRR of 6.07% against a 10% hurdle.
Project IRR
6.07%
Project NPV
$(15.68)m
DIF facility (1.30x DSCR)
$34.0m
Breakeven tariff
0.1009 /kWh
1
A $34.0m DIF facility is comfortably bankable
Flat 1.30x DSCR in every period, retired in Year 12 of a 15-year tenor.
2
But the asset returns 6.07% unlevered and 6.04% to equity
NPV of $(15.7)m against the 10% required return.
3
The gap is the tariff, not the structure
Breakeven needs 0.1009/kWh versus 0.0750 today — a 34.5% increase.
4
Recommendation: renegotiate tariff or EPC cost
Then bring the same financing structure back to committee unchanged.

## Slide 2
THE PROJECT AND THE INVESTMENT THESIS
A technically simple, contractually de-risked asset
Which is exactly why the tariff is the only variable that matters.
Capacity
50 MW solar, Rift Valley
Construction
$60.0m over 12 months
Operations from
1 January 2027
Annual generation
91.98 GWh
Offtake
20-yr take-or-pay PPA
Tariff
0.0750 /kWh, +1.5% p.a.
The thesis is binary
No fuel cost, no volume risk, no merchant exposure — and a Year 1 EBITDA margin of 82.6%. With no operating leverage to pull and no volume upside, there is nothing to optimise in operations. Value is set entirely by tariff versus capex.

## Slide 3
BASE-CASE PROJECT ECONOMICS
Stable, predictable cash flow — and not enough of it
CFADS averages $5.35m a year against debt service sculpted to exactly 1.30x cover.
Revenue, Yr 1 to Yr 20
$6.90m → $9.15m
CFADS, Yr 1 to Yr 20
$4.89m → $5.83m
Average CFADS
$5.35m
Lifetime generation
1,839.6 GWh
Payback / cash-on-cash
12 yrs / 1.78x
Note the squeeze: the tariff escalates at 1.5% a year but opex at 3.0%, so margin compresses slightly every year of the 20-year life.
Chart: CFADS vs total debt service (USD m)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
CFADS | 4.8889 | 4.9362 | 4.9837 | 5.0316 | 5.0798 | 5.1284 | 5.1772 | 5.2263 | 5.2757 | 5.3254 | 5.3753 | 5.4255 | 5.4759 | 5.5266 | 5.5775 | 5.6286 | 5.6799 | 5.7314 | 5.783 | 5.8348
Total debt service | 4.3248 | 4.3666 | 4.4087 | 4.4511 | 4.4937 | 4.5366 | 4.5798 | 4.6233 | 4.667 | 4.7109 | 4.7551 | 4.5602 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 4
2%
4%
6%
8%
10%
RETURNS VERSUS HURDLE
The project does not clear its hurdle rate
At 6.07% unlevered the project earns roughly four percentage points less than its own 10% discount rate.
10.00%
Required return
6.07%
Project IRR achieved
Net present value at 10%: $(15.68)m
Three levers to breakeven
PPA tariff
0.0750 → 0.1009 /kWh
+34.5%
Net capacity factor
21.0% → 28.2%
+7.2pp
Total capex
$60.0m → $42.03m
-30.0%
In practice only one of these is negotiable: the tariff, with the offtaker.

## Slide 5
WHAT WOULD HAVE TO BE TRUE
Only 3 of 49 scenarios clear a 10% return
All three sit in the top-right corner: it takes a better tariff AND a better resource together, not either alone.
PPA tariff (USD / kWh)
Net capacity factor
Range across the grid
Project IRR spans 0.9% to 11.2% across the full 7x7 range.
Only 3 of 49 clear 10%
Every one needs a capacity factor of 24.0% or better AND a tariff of 0.0850 or better — simultaneous outperformance on two independent variables.
Base case sits mid-grid
21.0% capacity factor at 0.0750/kWh returns 6.1%.
Capex is the cleaner lever
A $5m saving is worth c.0.8pp of IRR, and it is within the sponsor's control in a way the weather is not.
0.0600
0.0650
0.0700
0.0750
0.0800
0.0850
0.0900
16.5%
18.0%
19.5%
21.0%
22.5%
24.0%
25.5%
0.9%
1.7%
2.5%
3.2%
4.0%
4.7%
5.4%
1.8%
2.6%
3.4%
4.2%
5.0%
5.7%
6.4%
2.6%
3.5%
4.4%
5.2%
5.9%
6.7%
7.4%
3.4%
4.4%
5.2%
6.1%
6.9%
7.7%
8.4%
4.2%
5.2%
6.1%
6.9%
7.8%
8.6%
9.4%
5.0%
5.9%
6.9%
7.8%
8.6%
9.5%
10.3%
5.7%
6.7%
7.7%
8.6%
9.5%
10.3%
11.2%

## Slide 6
DIF FUNDING STRUCTURE — SOURCES AND USES
A $34.0m senior facility at 56.6% gearing
Well inside the NIF's 70% cap, leaving $8.03m of unused debt capacity.
$61.88m
$61.88m
DIF senior debt
$33.97m
Sponsor equity
$27.91m
Construction capex
$60.00m
Debt service reserve $1.88m
SOURCES
USES
Gearing achieved
56.6%
DIF gearing cap
70.0%
Unused debt capacity
$8.03m
Stated assumption
The DSRA is treated as equity-funded and outside the gearing base. This is the conservative reading, and is surfaced here rather than buried.

## Slide 7
$10m
$20m
$30m
$40m
DEBT SIZING — WHICH CONSTRAINT BINDS
The DSCR covenant binds, not the gearing cap
Cash flow is the limit on this facility, not policy.
$42.00m
$33.97m
70% gearing cap
permits
1.30x DSCR covenant
supports
BINDS
The lower of the two tests governs: we size at $33.97m.
Test 1 — gearing cap
70% of $60.0m of capex permits a facility of $42.00m.
Test 2 — covenant capacity
Discounting maximum affordable debt service (CFADS divided by 1.30x) at the 8.0% coupon over 15 years supports $33.97m.
Result
Sized at $33.97m; gearing settles at 56.6%, some $8.03m below the cap.
Read-across: the DIF cannot lend more even if it wanted to. The constraint is the asset's cash generation — which loops straight back to the tariff.

## Slide 8
DEBT SERVICE AND COVENANT PERFORMANCE
Flat 1.30x cover, and the facility retires in Year 12
Three years inside tenor. As a credit, this is clean.
Minimum DSCR
1.30x
Average DSCR
1.30x
DSCR incl. 50% sweep
1.13x
Facility repaid
Year 12 of 15
DSRA (six months)
$1.88m
The trade-off, stated plainly: zero headroom by construction
Sculpting to exactly 1.30x means any CFADS miss breaches on day one. We recommend resculpting at 1.40-1.45x and accepting a smaller facility.
Chart: DSCR profile vs the 1.30x covenant floor
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
DSCR (scheduled) | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A
Covenant floor | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A
DSCR incl. cash sweep | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1304 | 1.1898 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A

## Slide 9
0%
2%
4%
6%
RETURNS — AND WHY LEVERAGE IS NOT THE PROBLEM
After tax, the debt costs less than the asset earns
The capital structure is efficient. Both returns are simply too low.
Cost of DIF debt versus what the asset earns
After-tax cost of DIF debt (8.0% coupon less 30% shield)
5.60%
Unlevered return the asset earns
6.07%
Positive spread of 0.46pp — leverage adds value here.
Pre-empting the obvious challenge
Naive read: an 8.0% coupon against a 6.07% asset return must destroy equity value. Wrong — interest is deductible, and the shield is worth $6.15m over the life.
Project IRR
6.07%
plus tax shield
$6.15m over life, 30.0% of $20.50m interest paid
less DSRA drag
$1.88m idle for 12 years
Equity IRR (0.03pp below project)
6.04%
Gearing is not the lever. The tariff is.

## Slide 10
RISKS AND MITIGANTS
Two risks matter before financial close
A single offtaker carrying all the debt service, and a resource estimate with no margin for error.
RISK 1
Offtaker credit and payment
All debt service rests on one counterparty under a 20-year take-or-pay PPA, and the structure is sized to exactly 1.30x. There is 0.00x of headroom, so a payment delay is an immediate breach.
MITIGANTS
Sovereign or Treasury payment guarantee
Letter of credit covering three to six months of invoicing, on top of the DSRA
Liquidity facility or covenant reset mechanism
Resculpt at 1.40-1.45x for genuine headroom, accepting a smaller facility
RISK 2
Resource and capex
The 21% net capacity factor is a single point estimate with no degradation allowance, and a 6.07% IRR absorbs neither a resource shortfall nor an overrun. A $5m overrun costs c.0.8pp of IRR.
MITIGANTS
Independent P50/P90 yield study, with debt sized off P90
Fixed-price, date-certain turnkey EPC with liquidated damages
5-10% contingency inside the capex line
Inverter replacement reserve funded from operating cash from c.Year 8

## Slide 11
THE ASK AND NEXT STEPS
We are not asking for credit approval today
We are asking for a mandate to renegotiate the tariff, and authority to re-table this structure once it clears.
1
Approve an approach to the offtaker on tariff
Seek 0.1009/kWh, or a blended package of tariff plus capital contribution reaching the same NPV.
Deal team
Weeks 1-4
2
Commission an independent P50/P90 yield study
To be completed before any credit submission; debt to be sized off P90.
Technical adviser
Weeks 1-6
3
Re-tender the EPC scope
Test the $42.0m breakeven capex and whether the 30.0% saving is achievable.
Sponsor and EPC
Weeks 2-6
4
Return to committee with a revised base case
Same structure, new economics.
Deal team
Week 6
Hold the structure as-is — $34.0m at 56.6% gearing, sculpted to 1.40x. It is ready to execute the moment the economics clear.

## Slide 12
APPENDIX A1 | FULL DEBT AMORTISATION SCHEDULE
Senior debt outstanding, drawdown to repayment
Period-by-period drawdown, interest, principal, closing balance and DSCR.
Facility size
$33.97m
Coupon
8.0%
Tenor
15 years
Fully repaid
Year 12
Total interest paid
$20.50m
Source: Debt tab, rows 38-50.
Chart: Senior debt outstanding (USD m)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Senior debt outstanding | 32.3669 | 30.5896 | 28.6281 | 26.4673 | 24.091 | 21.4816 | 18.6203 | 15.4867 | 12.0587 | 8.3125 | 4.2224 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 13
APPENDIX A2 | CAPEX VERSUS CAPACITY FACTOR SENSITIVITY
Capex is the more powerful and more controllable lever
Useful if the EPC re-tender proposal is challenged.
$5m of capex saving
is worth roughly 0.8pp of project IRR — a materially steeper gradient than the resource assumption delivers.
Breakeven capex is $42.03m
a 30.0% reduction against the $60.0m budget, and the only breakeven lever that does not depend on the offtaker.
Capex is controllable
unlike the weather, it is testable through a competitive EPC re-tender with fixed-price, date-certain terms.
Grid 3 — Sensitivities L11:S18
Heat map to be dropped in once the grid values are shared.
Source: Sensitivities tab, Grid 3 (L11:S18).

## Slide 14
APPENDIX A3 | ASSUMPTIONS AND STATED JUDGEMENTS
Where the case was silent, we made the call explicit
The honesty slide. Each judgement below is a modelling choice, not a fact from the case.
Panel degradation
None applied. Generation is held flat at 91.98 GWh across the 20-year life.
Working capital
Assumed nil. No receivables or payables movement is modelled.
Maintenance capex
None modelled beyond the operating cost line.
DSRA treatment
Equity-funded and outside the gearing base — the conservative reading.
Tax in CFADS
Applied on an unlevered basis, so CFADS is independent of the financing structure.
Terminal value
Nil. No residual or repowering value is credited at Year 20.
Source: Assumptions tab, rows 47-57. Four further judgements are listed there in full.

## Slide 15
APPENDIX A4 | SCULPTED VERSUS LEVEL REPAYMENT
Why we sculpted, and what it costs in headroom
Held in reserve: the term sheet asked explicitly for justification of the profile choice.
Sculpted repayment (selected)
Principal is shaped to CFADS, so DSCR is flat at 1.30x in every period — minimum equals average.
Maximises debt capacity at a given covenant: no single weak year drags the sizing down.
Supports the full $33.97m facility and a Year 12 retirement with the 50% sweep.
Cost: zero headroom by construction. Any CFADS miss breaches on day one.
Level repayment (rejected)
Equal principal instalments ignore the CFADS profile, so DSCR varies period to period.
The binding minimum DSCR falls below 1.30x in the early years, forcing a smaller facility.
Simpler to administer, but it buys headroom by lending less rather than by lending better.
Trade-off: more comfort per period, less debt raised and a longer equity payback.